## Slide 1: OBC
Presented by:
Moses Mulwa | Alex Ngibuini | Brian Nzangi

## Slide 2: OBC Functions
•Recording and storage of telemetry and satellite payload data.
•Encoding and decoding of data packets to and from the ground station.
•Processing of commands from the GS.
•Monitoring other subsystems.
•Implementing watchdog functions.
•Controlling the orientation of the satellite within its orbit.

## Slide 3: OBC architecture
Processing architecture
Could be centralized to reduce BOM count, complexity and power consumption compared to a distributed architecture.
Software Architecture
A kernel such as FreeRTOS would be suitable as it is thoroughly tested and has been used in space applications.
Software Communication Framework
RS485 to be used for communication between subsystems

## Slide 4: Some processor requirements
1. High fault-tolerance
This could be achieved by: ECC, CRC modules, Lock-step architecture.
2. Radiation/ionization tolerance
This could be achieved by selecting a radiation hardened chip or having external shielding to minimize SEU, SEL and ionization effects.
3. Floating point precision
Is necessary since some satellite processes require a lot of floating-point calculations. This requires an FPU(single/double precision) and/or DSP slices.
4. Low current consumption
This makes MCUs with low power modes a good option.

## Slide 5: I/O
Table 1: Comparison of possible I/O and their applications
Protocol | Data link | Signalling rate | Possible application
SpaceWire | LVDS | Up to 400Mbps | Camera payload
CAN | CAN | Up to 1Mbps | Communication
USB | USB | Up to 480Mbps | External storage/ debugging
RS-232 | UART/USART | Up to 1Mbps | EPS
RS-485 | UART/USART | Up to 35Mbps | EPS/ADCS
I2C | 12C | Up to 3.4Mbps | Sensors/ADCS
SPI | SPI | Up to 60Mbps | Camera payload

## Slide 6: MCU – STM32H743 microcontroller
Features:
ARM Cortex-M7
2MB flash, 1MB SRAM, 32-bit EMIF
Max. clock frequency of 480MHz
CRC calculation unit
4X UART, 6X SPI, 2X CAN, 4X I2C, 2X USB, HDMI
DP-FPU, and DSP
Memory Protection Unit
168 GPIO
Max current consumption 840mA
Unit cost: $44.89
Flight heritage on 6U M6P CubeSat launched in 2019
In stock at LCSC
Fig 3: STM32H743 from STMicroelectronics

## Slide 7: STM32H743 Specifications
Weight
3g
Size
14 x 14 mm
Package
LQFP-100
Fig 4: STM32H755 development kit

## Slide 8: STM32H743 Development
Hardware Development
Development kits for prototyping are available starting from $28.42
Reference designs are provided by ST
Software Development
STM32 CubeIDE by ST supports the STM32H743. It allows for code editing, debugging, code generation and run-time resource estimation.
HAL libraries are available.
FreeRTOS is supported.
Programmer’s manuals, application notes are in plenty.
An existing developer community has been identified with a discussion forum at Community.St and Electronics Stack Exchange.
Fig 4: STM32H755 development kit

## Slide 9: OBC
Communication Protocol
RS485 was chosen as the communication protocol to be used between subsystems. Other sensors and devices will use their default protocols.
Transceivers for the RS485 have been chosen.
Storage
A 128 GB SD card was chosen. An SD Card Mount will also be included to facilitate this.
Memory
A 2 Mb FRAM will be added to supplement the existing RAM capabilities.

## Slide 10: OBC
Extra devices needed for MCU support
VDDA Filters, HSE and LSE Oscillators, Capacitors e.t.c have been added.
Sensors
Current, Temperature sensors have been chosen to aid in system status monitoring.
Redundancy
A VBAT has been added to power the real time clock and SRAM if VDD goes low.

## Slide 11: OBC
Redundancy
All OBC components will have spares for testing and also to aid in situations of failure.

## Slide 12: OBC
Weight
The OBC system has a maximum of about 100g. All components have about 50g. Even after adding connectors, PCB etc. The weight will not surpass 150g.
Size
PC104 (90 × 96 mm) with a height of about 15 mm
Price
$100 per system. For redundancy, three systems will be made.
Manufacturer
JLCPCB has been chosen as the PCB Manufacturer and LCSC as the part supplier.

## Slide 13: OBC Challenges
Complexity
Due to it’s central nature to the entire satellite, it tends to be a complex system to design and monitor.

## Slide 14
Thank You